## Slide 1: Microcontroller
By Parikshit Saha

## Slide 2: What is Microcontroller?
A microcontroller is basically a computer which is placed on a single integrated circuit chip. It consists of memory, a processor, as well as input-output interfaces. Microcontrollers are programmed to run a certain task, which means, if there is a need to change or enhance its functionality, one must install a new program on the chip.
Microcontrollers can be found in a variety of everyday items: household appliances (e.g. microwave ovens, TV-sets), toys (Lego NXT, talking dolls), vehicles (cars, hoists), etc. Microcontrollers’ wide usage has been possible because they are easy to program and have a wide range of functionalities

## Slide 3: What is Arduino?
Arduino is open-source hardware which consists of ATMEL microcontroller based programmable circuit board and a easy to use Software IDE (Integrated Development Environment) that runs on your computer.

## Slide 4: Basic features of Arduino UNO
Microcontroller | ATmega168/328
Operating Voltage | 5V
Input Voltage (recommended) | 7-12V
Input Voltage (limits) | 6-20V
Digital I/O Pins | 14 (of which 6 provide PWM output)
Analog Input Pins | 6
DC Current per I/O Pin | 40 mA
DC Current for 3.3V Pin | 50 mA
Flash Memory | 16 KB (ATmega168) or 32 KB (ATmega328) of which 2 KB used by bootloader
SRAM | 1 KB (ATmega168) or 2 KB (ATmega328)
EEPROM | 512 bytes (ATmega168) or 1 KB (ATmega328)
Clock Speed | 16 MHz

## Slide 5: Simplified AVR Architecture

## Slide 6: Arduino Pin Diagram

## Slide 7: Port Pin Directionality
Input/output from Arduino’s Perspective
pinMode(Pin, Mode)
For Sensor Pins Mode will be input i.e. data incoming (except vcc-gnd pins)
For Motor Pins Mode will be output i.e. data outgoing (except vcc-gnd pins)

## Slide 8: I/O Operations
digitalRead(Pin)
digitalWrite(Pin,State), State is 0(LOW) or 1(HIGH)
analogRead(Pin)
analogWrite(Pin, Value), Value is between 0 to 255

## Slide 9: Arduino Basic Coding Structure
<define global variables and include header files here>
  void setup() {
  < executed only once>
  < define input/output mode for digital pins > } void loop() {
  <infinite loop>
  <things like input from sensors, sending output etc. > }

## Slide 10: Led blink Arduino Demo

## Slide 11: dual color Led glow Arduino Demo

## Slide 12: Baud Rate & Bit Rate
Baud- Changes of Signal per second
Bit Rate- Nos of bits sent per second

## Slide 13: Serial Port Monitor
Serial.begin(speed)
Serial.read()
Serial.available()

## Slide 14: Serial Port Demos

## Slide 15: What is PWM & PWM Pin in Arduino?

## Slide 16: Sensor Interfacing with Arduino
By Parikshit Saha

## Slide 17: Sensor Interfacing
Sensors usually used to have 3 terminals Vcc, Gnd & Signal (either digital or analog)
Some of the sensors used to have 4 terminals with facility of both digital as well as analog signal read.

## Slide 18: Hall Sensor Interfacing

## Slide 19: Tilt Switch Interfacing

## Slide 20: Motor Interfacing with Arduino
By Parikshit Saha

## Slide 21: Types of Motors
DC Motor
Servo Motor
Stepper Motor

## Slide 22: DC Motor Interfacing
Dc Motor have two terminals vcc & gnd
Arduino directly can provide only 40mA of current within an max of 5V output which is insufficient to rotate the motor. So we need a specific type of circuit known as Motor Driver to drive the motor.
Some Dc Motor also has a higher V-I requirement based on torque of operation. (600mA, 4.5V to 36V)
H-bridge circuit is used.
Different types of H-bridge circuits are L293, L293D, L298
Some Advanced level H-bridge circuits are VNH2SP30, VNH5019 have the higher voltage- current motor driving capabilities.

## Slide 23: DC Motor Interfacing (contd.)
fhgfation

## Slide 24: What is Servo Motor?
3 Wire terminals vcc, gnd & signal
In signal terminal we feed angle of rotation in degree while using directly ‘servo.h’ Arduino library
Internally Dc Motor + Potentiometer

## Slide 25: Servo Motor Interfacing (from library function)

## Slide 26: Servo Motor Interfacing (building from scratch)

## Slide 27: Limitation & Solution to Overcome
High Torque Servo Motor Interfacing-
Direct Arduino I-O Pins can feed only 40mA of Current which is insufficient to rotate high torque servo motors (like mostly used MG995 Servo needs 170mA of current).
Generally High Voltage Input used to give high amount of current but as our servo motors are used to have a specific limited voltage of operation (like 5V for MG995 Servo), we use Step Down transformer circuit in between & connect +Vcc & GND terminal of the output with the servo directly while only the signal pin is feed from the Arduino. (N.B.- Common Ground between Arduino & Step Down Output is required)

## Slide 28: DC Motor with Encoder
By Parikshit Saha

## Slide 29: What is Encoder?
DC Motor has only two terminal Vcc & Gnd. So it’s impossible to control it’s movement or track it’s movement. Encoder helps us to resolve this issue.
Encoder is basically consists of an circular disk with specifically encoded pattern & an ir transmitter-receiver block.
Slots within the encoded pattern disk indicated the resolution of the encoder.
When the ir is blocked by encoder disk no signal is received by rx terminal & viceversa.

## Slide 30: Encoder ON-OFF Demo
fhgfation

## Slide 31: Encoder Counter Demo
fhgfation

## Slide 32: Limitation & Solution to overcome it
Availability of limited no of Analog & Digital Pins with Arduino Uno
Lower Specific Speed of Operation
Go for advanced version of Arduino like Arduino Mega which has more nos of I-O Pins
Use of Higher Processing Speed Arduino Variants Microcontroller Boards
Most of the Variant optional Boards (ex. NODE32 MCU) can also be program using Arduino IDE.

## Slide 33: Stepper Motor Interfacing
By Parikshit Saha

## Slide 34: What is a Stepper Motor? Why Stepper Motor?

## Slide 35: What is a Stepper Motor? Why Stepper Motor?

## Slide 37: Clock Generator Circuit using NE555 Timer IC

## Slide 38: JK Flipflop

## Slide 39: Stepper Motor Driver Circuit

## Slide 40: Arduino Based Stepper Motor Control

## Slide 41: Interfacing Code without library use
<<REFER THE LAB MANUAL>>

## Slide 42: Interfacing Code using Stepper.h Library
#include <Stepper.h>
const int stepsPerRevolution = 200; // change this to fit the number of steps per revolution
Stepper myStepper(stepsPerRevolution, 8, 9, 10, 11);
void setup() {
myStepper.setSpeed(60);
Serial.begin(9600);
}
void loop() {
Serial.println("clockwise");
myStepper.step(stepsPerRevolution);
delay(500);
Serial.println("counterclockwise");
myStepper.step(-stepsPerRevolution);
delay(500);
}
For More Specific Control you can use AccelStepper.h Library

## Slide 43: Stepper Motor Advantages
It is very safe to use.
It is very easy to setup.
It provides with highly controlled movement.
The Stepper motors have very long life, only if you don’t break it by an accident.
It is an excellent repeater device it can repeat its movements very accurately.
Stepper motor is also very cheap as compared to other motion controlling devices.
One of the main features of stepper motor is that it can’t be damaged by overloading.
When overloaded it stops working until the load is removed.
It is easy to operate.
It offers very precise movement.

## Slide 44: Stepper Motor Applications
Step motors are used every day in both industrial and commercial applications because of their low cost, high reliability, high torque at low speeds. For making more advanced technologies we use stepper motors rather than simple motors. Computer-controlled stepper motors are a type of motion-control positioning system. Step Motors are typically digitally controlled motors, for use in holding or precise positioning applications. These motors are used at;
Industrial Machines : CNC Machines, Milling Machines, Laser Cutters etc,
Computer Technology: CD-Roms, DVD Players, Floppy Disk Drives, Scanners etc.
Printing : Printers, Plotters, 3D Printers etc.
Intelligent Lighting Systems : Lasers, Optical Devices, Mirror Mounts